Annex  No 1

The name and seat of the Contractor:

……………………………………………………………………………………….…

……………………………………………………………………………………….…

……………………………………………………………………………………….…

REGON: …………………………..

VAT ID: ………………………………..

TEL: ………………………………………

FAX: …………………………………..

e-mail: ……………………………..……

OFFER FORM

Referring to the offer inquiry No. 1/2019 / CuBR

Object of the contract: delivery

for the task titled "Development of a wireless communication system in underground excavations, with particular emphasis on communication and data transmission in the area of exploitation in a pillar-chamber system" implemented as part of the CuBR program

We, the undersigned:

……………………………………………………………………………………………………………………………………………………………………………………

……………………………………………………………………………………………………………………………………………………………………………………

acting on behalf of and on behalf of:

……………………………………………………………………………………………………………………………

……………………………………………………………………………………………………………………………

……………………………………………………………………………………………………………………………

(name (company), exact address of the Contractor / Contractors)

We place an offer to perform the order in accordance with the description of the subject of the order contained in Annex 2 to the invitation to submit offers, and table No. 1 of this form:

| Offer parameters |
| --- |
| The date of the offer preparation |  |
| The offer expiration date |  |
| Reference to the criteria for the selection of the offer |
|  | Net price (PLN) |
| 1. Access point (2 pcs) |  |
| 2. Access point (18 pcs.) |  |
| 3. Software (firmware) Access points |  |
| 4. Controller of Access Points |  |
| 5. Network management software |  |
| Total net offer price (PLN) |  |
| In words: |  |
|  | Gross price (PLN) |
| 1. Access point (2 pcs) |  |
| 2. Access point (18 pcs.) |  |
| 3. Software (firmware) Access points |  |
| 4. Controller of Access Points |  |
| 5. Network management software |  |
| Total price of the gross offer (PLN) |  |
| Słownie: |  |
|  | VAT |
| VAT % |  |
| VAT (PLN) |  |
| VAT In words |  |
| Terms of implementation and date of payment |
| Delivery time |  |
| Payment deadline |  |

Tenderer's declaration:

We declare that:

- we have read the terms of the contract, we do not raise any objections to them, we consider them to be bound by the provisions laid down in them.

- our offer includes all elements specified in the Inquiry,

- we undertake to perform the order being the subject of this request for proposals by ..................................

- we consider ourselves to be bound by this offer for a period of 30 days from the deadline for submission of offers. We will provide warranty services during the warranty period

- we undertake to provide the Employer with all the certificates required by the regulations

| Name of the person authorized to submit the offer |  |
| --- | --- |
| Date and signature |  |

.

Attachments:

a) ……………………………………….			pages …………………….

b) ……………………………………….			pages …………………….

c) ……………………………………….			 	pages …………………….

TABLE 1. STATEMENT OF PARAMETERS

Hirschmann wireless devices with software (firmware) or equivalent

- Access point with parameters (2 pcs.)

| Lp | Name | Minimum parameters | Parameters offered |
| --- | --- | --- | --- |
| 1 | Port type and quantity | M12 A-Coded |  |
|  |  | X- LAN combo port: 10/100/1000BASE-TX |  |
|  |  | X- LAN combo port: SFP-1000BASE-SX/LX |  |
| 2 | Power supply | Double redundant |  |
| 3 | Radio Standard | IEEE802.11a/b/g/h/n WLAN interface as per IEEE802.11n |  |
|  |  | up to 450MBit/s gross bandwidth. |  |
| 4 | Supported Radio Standards | 1st WLAN interface as per IEEE802.11n |  |
|  |  | 2nd WLAN interface as per IEEE802.11n |  |
| 5 | Configuration interface COM | V.24 Interfejs |  |
|  |  | M12 A-Coded |  |
| 6 | Antenna connector | N socket |  |
|  |  | 3 x MiMo antenna connectors |  |
| 7 | Frequency band Supports | 2.4 GHz and 5 GHz: 2400 -2483.5 MHz (ISM) and 5170 - 5850 MHzSupports 2.4 GHz and 5 GHz: 2400 -2483.5 MHz (ISM) and 5170 - 5850 MHz |  |
| 8 | Modulation | 22M0F7D (DSSS/OFDM) at 2.4 GHz |  |
|  |  | GHz20M0G7D (OFDM) at 5 GHz |  |
| 9 | Encryption | IEEE 802.11i / WPA2 with passphrase or 802.1x and hardware-accelerated AES, closed network, WEP64, WEP128, WEP152, , user authentication, 802.1x /EAP, LEPS, WPA1/TKIP. |  |
| 10 | Operating voltage | 24/36/48 VDC (18-60 VDC) |  |
| 11 | Operating temperature | -40 ºC …… 70 ºC |  |
| 12 | Relative humidity (non-condensing): | 10% ... 95% |  |
| 13 | MTBF | No less than 58 years (MIL-HDBK-217F) |  |
| 14 | Protective paint on PCB | Yes (conformal coating) |  |
| 15 | Dimensions (W x H x D) | No more than 311 mm x 219 mm x 75 mm |  |
| 16 | Protection class | IP 67 |  |
| 17 | Approvals | CE, EN 60950-1, RED-EN 300 328 (2,4 GHz), EN 301 893 (5 GHz), EN 302 502 (5,8 GHz), EN 301 489-1, EN 301 489-17, ANSI / ISA 61010-1; CSA klasa1 div2; FM3611 klasa 1 div.2 |  |

- Access point with parameters (18 pcs.)

| Lp | Name | Minimum parameters | Parameters offered |
| --- | --- | --- | --- |
| 1 | Port type and quantity | M12 X-Coded |  |
|  |  | 1 port LAN 10/100/1000BASE-TX |  |
|  |  | Power over Ethernet IEEE 802.3af |  |
| 2 | Power supply | M12 5 Pin A-Coded |  |
| 3 | Radio Standard | IEEE802.11a/b/g/h/n WLAN interface as per IEEE802.11n |  |
|  |  | up to 450MBit/s gross bandwidth. |  |
| 4 | Supported Radio Standards | 1st WLAN interface as per IEEE802.11n |  |
|  |  | 2nd WLAN interface as per IEEE802.11n |  |
| 5 | Configuration interface COM | V.24 Interfejs |  |
|  |  | M12 A-Coded |  |
| 6 | Antenna connector | N socket |  |
|  |  | 3 x MiMo antenna connectors |  |
| 7 | Frequency band Supports | 2,4 GHz i 5 GHz: 2400 -2483,5 MHz (ISM), 5170 - 5850 MHz |  |
| 8 | Modulation | 22M0F7D (DSSS / OFDM) at 2,4 GHz |  |
|  |  | 20M0G7D ( OFDM) at 5 GHz |  |
| 9 | Encryption | IEEE 802.11i / WPA2 with passphrase or 802.1x and hardware-accelerated AES, closed network, WEP64, WEP128, WEP152, , user authentication, 802.1x /EAP, LEPS, WPA1/TKIP. WPA1 / TKIP |  |
| 10 | Operating voltage | Range 16.8 - 32V VDC, Power over Ethernet according to IEEE 802.3af |  |
| 11 | Operating temperature | -40 ºC do 70 ºC |  |
| 12 | Relative humidity (non-condensing): | 10% ... 95% |  |
| 13 | MTBF | No less than 58 years (MIL-HDBK-217F) |  |
| 14 | Protective paint on PCB | Yes (conformal coating) |  |
| 15 | Dimensions (W x H x D) | No more than 261 x 189 x 55 mm |  |
| 16 | Protection class | IP 67 |  |
| 17 | Approvals | EN 60950, EN 300328, EN 301893, UL60950, EN 61000-6-2, EN 61131, E1 i EN 50155 |  |

3. Software (firmware) Access points

| REQUIRED SOFTWARE FEATURES | OFFERED SOFTWARE FEATURES |
| --- | --- |
| Fully independent configuration of two radio interfaces |  |
| Parallel operation of two radio interfaces on the same frequency band |  |
| Centralized management from the WLC controller (Wireless Lan Controller) |  |
| Automatic creation of backbone network connections in the tree topology |  |
| SSID of the backbone network depending on the depth of the tree: SSID-0, SSID-1, ..., SSID-7 |  |
| Any wireless connection between the AP in the backbone on another radio channel |  |
| Automatic reconstruction of the network in the event of a failure, loss of connection |  |
| Quick reconfiguration of the network topology |  |
| Ability to specify the minimum signal strength required to establish a connection |  |
| Building a network of connections through SSID priorities, signal strength |  |
| Detection of a damaged cable connection |  |
| Disabling radio interfaces after detecting cable connection failure |  |
| Creating a backbone and access network |  |
| Automatically disable broadcasting of an access and backbone network in the event of a connection loss |  |
| Automatic activation of broadcasting of access and backbone network in the event of connection to the network. |  |
| Monitoring network connection, detecting its absence, Alive Test Ping |  |
| Time of interruption in the Client's UDP traffic in case of AP power loss (switching the client to another AP) - no more than 530ms. |  |
| Time of interruption in the Client's UDP traffic in case of AP-powered return (client switching to AP) - no more than 40ms.. |  |
| Time of interruption in the Customer's UDP traffic at the depth of the network of connections +1 in the event of loss of AP power (switching the client to another AP) - no more than 600ms. |  |
| Time of interruption in the Customer's UDP traffic at the depth of the connection network +1 in case of AP-powered return (client switching to AP) - no more than 190 ms |  |
| Fast Roaming |  |
| COM port server function |  |

4. Access point controller

| Lp | Name | Minimum parameters | Parameters offered |
| --- | --- | --- | --- |
| 1 | Access point controller | Minimum number of access points – 50 |  |
|  |  | Ethernet ports: Not less than 4 pcs. 10/100/1000 Mbit / s |  |
|  |  | HiSpeed ​​USB port for USB printer (Print Server) |  |
|  |  | COM configuration port |  |
|  |  | Power supply: 110V-230V |  |
|  |  | Working temperature: 5 ºC ... 40 ºC |  |
|  |  | Relative humidity (non-condensing): 10% ... 95% |  |
|  |  | Dimensions (width X height x depth): No more than 435 x 45 x 207 mm |  |
|  |  | MTBF - Not less than 300000 h |  |

5. Network management and monitoring software

| REQUIRED SOFTWARE FEATURES | OFFERED SOFTWARE FEATURES |
| --- | --- |
| License for not less than 64 Nody |  |
| Possibility to upgrade the license for a larger number of Nodes |  |
| Supported platforms, Windows / Linux |  |
| Configuration wizard |  |
| Support for SNMP v1 / 2/3 |  |
| LLDP protocol support |  |
| Automatic detection of devices in the network |  |
| Distributed network management with hierarchical work levels |  |
| Drawing and visualization of network topology |  |
| Mass configuration of devices |  |
| Condition monitoring and device operation |  |
| Network failure reporting (SNMP trap |  |
| Automatic configuration backup |  |
| Control of the configuration signature monitoring changes in the device configuration files |  |
| Alerts regarding unauthorized changes to the system |  |
| User roles for controlled access |  |
| History of events in a graphical format |  |
| VLAN browser, MIB viewer, edit and start mode |  |
| Simultaneous device upgrade |  |
| OPC server |  |
| Possibility of direct configuration of devices from the program level |  |
| Generating network inventory reports |  |

The offers will be only taken into account in a complete manner corresponding to the content of this inquiry, i.e. the offer must include the bidder's reply to each of the points listed above.